# APPENDICES

# APPENDIX I

# ALGORITHMS FOR CHOOSING THE OPTIMAL

# ALGORITHM-1  LMS and  RLS

% Set up parameters.

M = 2; % Alphabet size for modulation

sigconst = qammod(0:M-1,M); % Signal constellation for 16-QAM

chan = [1 0.45 0.3+0.2i]; % Channel coefficients

% Set up equalizers.

eqrls = lineareq(6, rls(0.99,0.1)); % Create an RLS equalizer object.

eqrls.SigConst = sigconst; % Set signal constellation.

eqrls.ResetBeforeFiltering = 0; % Maintain continuity between iterations.

eqlms = lineareq(6, lms(0.003)); % Create an LMS equalizer object.

eqlms.SigConst = sigconst; % Set signal constellation.

eqlms.ResetBeforeFiltering = 0; % Maintain continuity between iterations.

eq_current = eqrls; % Point to RLS for first iteration.

% Main loop

for jj = 1:4

msg = randint(500,1,M); % Random message

modmsg = qammod(msg,M); % Modulate using 8-QAM.

% Set up training sequence for first iteration.

if jj == 1

ltr = 200; trainsig = modmsg(1:ltr);

else

% Use decision-directed mode after first iteration.

ltr = 0; trainsig = [];

end

% Introduce channel distortion.

filtmsg = filter(chan,1,modmsg);

% Equalize the received signal.

s = equalize(eq_current,filtmsg,trainsig);

% Plot signals.

h = scatterplot(filtmsg(ltr+1:end),1,0,'bx'); hold on;

scatterplot(s(ltr+1:end),1,0,'g.',h);

scatterplot(sigconst,1,0,'k*',h);

legend('Received signal','Equalized signal','Signal constellation');

title(['Iteration #' num2str(jj) ' (' eq_current.AlgType ')']);

hold off;

% Switch from RLS to LMS after second iteration.

if jj == 2

eqlms.WeightInputs = eq_current.WeightInputs; % Copy final inputs.

eqlms.Weights = eq_current.Weights; % Copy final weights.

eq_current = eqlms; % Make eq_current point to eqlms.

end

end

ALGORITHM-2 Channel Equalizer Algorithm

function []=chan_equalizer1()

n = 200; % Number of symbols in each iteration

numiter = 25; % Number of iterations

M = 4; % Use 4-PSK modulation.

const = pskmod(0:M-1,M); % PSK constellation

chcoeffs = [1 ; 0.25]; % Channel coefficients

chanest = chcoeffs; % Channel estimate

tblen = 10; % Traceback depth for equalizer

nsamp = 1; % Number of input samples per symbol

sm = []; ts = []; ti = []; % Initialize equalizer data.

% Initialize cumulative results.

fullmodmsg = []; fullfiltmsg = []; fullrx = [];

for jj = 1:numiter

msg = randint(n,1,M); % Random signal vector

modmsg = pskmod(msg,M); % PSK-modulated signal

filtmsg = filter(chcoeffs,1,modmsg); % Filtered signal

% Equalize, initializing from where the last iteration

% finished, and remembering final data for the next iteration.

[rx sm ts ti] = mlseeq(filtmsg,chanest,const,tblen,...

'cont',nsamp,sm,ts,ti);

% Update vectors with cumulative results.

fullmodmsg = [fullmodmsg; modmsg];

fullfiltmsg = [fullfiltmsg; filtmsg];

fullrx = [fullrx; rx];

end

% Compute total number of symbol errors. Take the delay into account.

numsymerrs = symerr(fullrx(tblen+1:end),fullmodmsg(1:end-tblen))

% Plot signal before and after equalization.

h = scatterplot(fullfiltmsg); hold on;

scatterplot(fullrx,1,0,'r*',h);

legend('Filtered signal before equalization','Equalized signal',...

'Location','NorthOutside');

hold off;

ALGORITHM-3 Linear Equalizer Algorithm

% Set up parameters and signals.

M = 4; % Alphabet size for modulation

msg = randint(1500,1,M); % Random message

modmsg = pskmod(msg,M); % Modulate using QPSK.

trainlen = 500; % Length of training sequence

chan = [1 ; 0.25]; % Channel coefficients

filtmsg = filter(chan,1,modmsg); % Introduce channel distortion.

% Equalize the received signal.

eq1 = lineareq(8, lms(0.01)); % Create an equalizer object.

eq1.SigConst = pskmod([0:M-1],M); % Set signal constellation.

[symbolest,yd] = equalize(eq1,filtmsg,modmsg(1:trainlen)); % Equalize.

% Plot signals.

h = scatterplot(filtmsg,1,trainlen,'bx'); hold on;

scatterplot(symbolest,1,trainlen,'g.',h);

scatterplot(eq1.SigConst,1,0,'k*',h);

legend('Filtered signal','Equalized signal',...

'Ideal signal constellation');

hold off;

% Compute error rates with and without equalization.

demodmsg_noeq = pskdemod(filtmsg,M); % Demodulate unequalized signal.

demodmsg = pskdemod(yd,M); % Demodulate detected signal from equalizer.

[nnoeq,rnoeq] = symerr(demodmsg_noeq(trainlen+1:end),...

msg(trainlen+1:end));

[neq,req] = symerr(demodmsg(trainlen+1:end),...

msg(trainlen+1:end));

disp('Symbol error rates with and without equalizer:')

disp([req rnoeq])

# APPENDIX II

# MAIN PROGRAM FOR NEURAL NETWORK BASED EQUALIZER

clc;

M = 4;  msg = randint(150,1,M); % Random message

modmsg = pskmod(msg,M);  % Modulate using QPSK.

plot(modmsg,'*')

hold on

trainlen =100; % Length of training sequence

%chan = [.986; .845; .237; .123+.31i]; % Channel coefficients

chan = [.986; .845; .237];

filtmsg = filter(chan,1,modmsg); % Introduce channel distortion.

plot(filtmsg,'o')

hold

% Equalize the received signal.

eq1 = lineareq(5, lms(0.01)); % Create an equalizer object.

eq1.SigConst = pskmod([0:M-1],M); % Set signal constellation.

%[symbolest,yd] = equalize(eq1,filtmsg,modmsg(1:trainlen)); % Equalize.

[symbolest,yd] = equalizem1(eq1,filtmsg,modmsg(1:trainlen)); % Equalize.

% Plot signals.

h = scatterplot(filtmsg,1,trainlen,'bx'); hold on;

scatterplot(symbolest,1,trainlen,'g.',h);

scatterplot(eq1.SigConst,1,0,'k*',h);

legend('Filtered signal','Equalized signal',...

'Ideal signal constellation');

hold off;

pause

% Compute error rates with and without equalization.

demodmsg_noeq = pskdemod(filtmsg,M); % Demodulate unequalized signal.

demodmsg = pskdemod(yd,M); % Demodulate detected signal from equalizer.

[nnoeq,rnoeq] = symerr(demodmsg_noeq(trainlen+1:end),...

msg(trainlen+1:end));

[neq,req] = symerr(demodmsg(trainlen+1:end),...

msg(trainlen+1:end));

disp('Symbol error rates with and without equalizer:')

disp([req rnoeq])

function [symbolEst, symbolDet, symbolErr] = thisequalizeneural1(eqObj, inputSig, trainSig);

% Extract equalizer object parameters.

alg = eqObj.AdaptAlg;

nWeights = eqObj.AdaptAlg.nWeights;

nSampPerSym = eqObj.nSampPerSym;

sigConst = eqObj.SigConst;

blindMode = eqObj.AdaptAlg.BlindMode;

% Derive signal dimensions.

nSamples = length(inputSig);

nSymbols = ceil(nSamples/nSampPerSym);

nTrain = length(trainSig);

delay = floor(eqObj.RefTap-1)/nSampPerSym;

x = flipud(reshape(inputSig, [nSampPerSym nSymbols]));

if nTrain > nSymbols - delay

warning('comm:equalize:trainSigLength', ...

['TRAINSIG will be truncated to a length equal to '...

'length(INPUTSIG)- delay, where delay = '...

'(EQOBJ.RefTap-1)/EQOBJ.nSampPerSym.']);

end

% Initialize symbol estimates and errors.

symbolEst = zeros(nSymbols, 1);    % symbol estimate vector

symbolDet = zeros(nSymbols, 1);    % detected symbols vector

symbolErr = zeros(nSymbols, 1);    % symbol error vector

% Reset channel if required.

if eqObj.ResetBeforeFiltering

reset(eqObj);

end

% Indices for input buffer, u, and decision sample, d.

% - i1 is the input buffer index for the current input signal sample:

%      u(i1)=sample; see below

% - nn1 and nn2 are input buffer indices used to perform the

%   sample shifting operation each equalizer iteration:

%      u(nn2)=u(nn1); see below.

% - id is an "index" into the decision value:

[i1, nn1, nn2, id] = eqindices(eqObj);

% Initialize input buffer, accounting for reference tap delay.

% Get current equalizer weights.

w = eqObj.Weights';  % Use hermitian transpose for mathematical simplicity.

u = eqObj.WeightInputs.';

% Constellation-related parameters.

conjConst = conj(sigConst);

constParam = 0.5*real(sigConst.*conjConst);

% Initial decision value (required for compatibility with DFE).

%dref = eqObj.dref;

if blindMode

if var(abs(sigConst))>eps

warning('comm:equalize:CMAsigconst',...

['Signal constellation with non-constant magnitude '...

'may cause CMA equalizer to be unstable.'])

end

% Set CMA constant

R2 = mean(abs(sigConst).^4)/mean(abs(sigConst).^2);

end

%---------------------------------------------------------------------%  Main loop.

N1=5; N2=16;M=N2+1; w1=0.2*rand(N1,N2); w2=0.02*rand(N2,M); a=0.02; eq='neuro';

pause

length(trainSig)

for ni=1:10

for n = 1:nSymbols

u(nn2) = u(nn1);             % shift input signal buffer samples

%  u(i1) = [x(:, n); dref(id)]; % current input signal vector

u(i1) = [x(:, n)]; % current input signal vector

if eq=='neuro'

%   [y,yn,net,w1,w2]=neuralm2(N1, N2, w1,w2,u);

[y,yn,net,w1,w2]=neural_abs(N1, N2, M,w1,w2,x);

else

y = w'*u;            % current output symbol (note hermitian transpose)

end

% Find closest signal constellation point (detector/slicer).

[minMetric, idx] = min(constParam - real(y*conjConst));

d = sigConst(idx);

% Symbol error for training/blind mode or decision-directed mode.

if ~blindMode

m = n - delay;

if m >= 1 && m <= nTrain

dref = trainSig(m);  % training mode

else

dref = d;  % decision-directed mode

end

e = dref - y;

else

dref = d;  % required for DFE

e = y .* (R2 - abs(y).^2); % blind mode (CMA)

end

%[m nTrain delay trainSig(m)  d]

[n y  dref   e]

%  pause

if isinf(e) || isnan(e)

warning('comm:equalize:error',...

['Equalizer unstable. ' ...

'Try adjusting step size or forgetting factor.']);

end

% Update weights until exhausted input samples. The weight update

% algorithm, update_weights, is a UDD method. That is, the method

% called will depend on the class of adaptive algorithm object.

if n<=nTrain

if eq=='neuro'

er=conj(e);

[w1,w2]=trainnm2(N1, N2,w1,w2,u,yn,a,er);

% [w1,w2]=train_abs(N1, N2, M,w1,w2,u,yn,a,er);

else

w=update_weights1(alg, w, u, e);

end

end

% Assign outputs and symbol error.

symbolEst(n) = y;

symbolDet(n) = d;

symbolErr(n) = e;

end

end

trainSig

[symbolEst     symbolDet ]

pause