PREAMBLES

SECTION 1 - GENERAL

A.	General

The Contract shall be a Remeasured Contract based on Drawings, Specifications and Bills of Quantities.

The Contractor is advised to carefully comprehend his contractual obligations under the provisions of the above contract and fully understand the proposed Scope of Works.

It is the Contractor's responsibility to insert the correct rates against each item in the unit rate column of the Bills of Quantities. Omitted items or incorrectly inserted rate shall be the sole responsibility of the Contractor.

These Preamble clauses shall be read in conjunction with the Conditions of Contract, Tender Drawings and Specifications, and they shall not be considered as exhaustive but merely as highlighting certain points. These documents shall be taken as mutually explanatory of one another.

B.	Units of Measurement and Abbreviations

All units of measurement shall be based on the Metric System of weights and measurements except where other units are specifically mentioned for standard products.

The metric terms and symbols occurring in the Contract Documents are based on the "System Internationale d'Unites (S.I. System)".

Abbreviation              Definition

m                     	linear metre

m2                    	Square metre

m3                    	cubic metre

kg                    	kilogramme

mm                    	millimetre

cm                    	centimetre

nr/no                    	number

LS                    	Lump Sum

JD	             	Jordan Dinars

BS                    	British Standard

ASTM                  	American Society for Testing and Materials Standards

Min.                  	Minimum

Max.                  	Maximum

Qty.                  	Quantity

Drg.                  	Drawing(s)

dia.or             	Diameter

Cont'd                	Continued

Spec.                 	Specification

MS	                  	Measured Separately

HVAC                  	Heating, Ventilation and Air

conditioning

Description of Items

Description of work and materials given in the Specifications and Drawings are not necessarily repeated in the Bills of Quantities. Trade preambles are not necessarily restricted to specific Bills but shall be held to apply throughout the Documents.

Any discrepancy between the Contract Documents shall be brought to the notice of the Engineer in writing for his decision as to which is the correct interpretation before the work is commenced.

Unless otherwise described, description shall be deemed to include for all sundry labours including cutting and fitting, notching, forming or cutting holes, chasing, angles, ends, short lengths, circular work, and the like as shown on Drawings, or required by the Specifications or the execution of the Works.

Pricing Generally

The Contractor shall satisfy himself as to the meaning of every item in the Bills of Quantities  and  rates inserted shall be deemed to cover all his contractual obligations under the Contract and all items necessary for the proper construction, completion and maintenance of the Works.

Rates shall include but not be limited to:-

- Payment of all state dues, duties, fees and charges, customs or other import duties, harbour wharfage and port dues, landing, quay and storage charges and any other local charges or dues applicable on all plant and materials imported for the purpose of incorporating the same into the Works.

- Engagement of expatriate staff including their messing and accommodation, air travel, insurances, indemnities, notices, leaves, sicknesses, income tax and any other fee or duty applicable on their salaries, repatriation of expatriates to country of recruitment.

- Rates shall also include for, but not be limited to, all temporary work required (including any that may be required by sub-contractors whether nominated or otherwise and other specialist Contractors under separate contract with the Employer), the provision and use of all plant required for carrying out the works in it's proper sequence, shifting, altering and adapting such temporary works and plant as may be required during the progress of the Works and removing at completion and making good any surface disturbed. No claim for additional payment will be allowed for any error or misunderstanding by the Contractor in this respect.

- The CONTRACTOR is advised to carefully comprehend his contractual obligations under the provisions of the above contract and fully understand the proposed Scope of Works.

SECTION 2 - CARPENTRY & JOINERY

A.	Wooden doors and the like have been enumerated.

B.	Timber shall be deemed to be wrought, i.e. planed finish, unless otherwise described.

Rates for carpentry and joinery items shall include:

C.	The preparation and submission of detailed shop drawings to the Engineer for approval, prior to the commencement of the work involved.

D.	Framing in the best manner and in accordance with the detailed Drawings, and for all labour, notching, cutting and waste, halvings, morticing, tenoning, wedging, scribing, openings, forming chamfers, grooves, rebates, rounded shapes, preparing surfaces to receive finishes, plugging to concrete and blockwork, making good all other sundry items of a like nature as required.

E.	Protecting all work liable to be damaged or as may be required by the Engineer and removing on completion.

F. 	For providing cramps, screws, nails and other fixing devices.

Rates for doors shall include for:

G.	Frames, sub-frames and fixing materials.

H.	Painting backs of frames with primer before fixing in position.

I.	ironmongery according to schedules including matching fixing screws, etc. and shall include removing before painting and then refixing.

J.	All necessary fixings, fittings, hanging, accessories and related works and materials;

K.	Preparing & painting or polishing/varnishing as indicated.

L.	Rates for glazed doors shall include glass and beads.

SECTION 3 - METAL WORK & GLAZING

A.	Aluminium curtain walling, doors, windows and the like have been enumerated or measured nett in square metre according to bills of quantities.

Rates for metal work shall include for:

B.	Assembling, cutting and waste, welding and grinding, drilling, counter sinking, bolting and riveting.

C. 	Shop coating with rust inhibitive primer, haulage, protection and storage.

D.	Aluminium sub-frames if and where required, hoisting and fixing in position, caulking with mastic, grouting mortices with cement and sand grout.

E.	Inspection of metal work at workshop by the Engineer if necessary.

F. 	Ironmongery as required including matching, fixing screws, etc. and shall include for fixing, removing before painting and then refixing.

G.	Approved design and quality weather and drought seals.

- Fly screens

- Aluminum or steel angles, profiles and frames

- All necessary fixings, fittings, accessories and related works and materials

L.	Preparation and submission of shop drawings and samples for Engineer's approval.

M.	Submitting detailed design criteria and calculations allowing for factors such as the size of panels, wind load, weight of glazing, etc. to substantiate the size, strength & design of the proposed extruded sections and thickness of glass.

Glazed Units

N.	Rates for glazed doors shall include glass, glazing accessories and beads as required.

P.	Rates for glazing work shall include for cutting to required sizes and shapes, forming holes, supplying and fixing all required gaskets, clips, beads, points, metallic putty, etc. protection of all glass from damage, replacing damaged panels, cleaning throughout and leaving all work in perfect condition.

Q.	Rates of galvanized work shall include for the treatment of cut ends, etc. as required.

Glazing - Generally

- Each kind of glass is given separately, stating the thickness. Glass with ground, sandblasted, embossed and engraved surfaces are each so described.

- Mirrors are enumerated.

Work is deemed to include:

- All necessary fixings, fittings, furniture, accessories and related works and materials,

- Stainless steel frames,

- Plywood backing

Ladders and the like

- Each kind of work is given separately, stating the kind of material and finish as delivered.  Staircases and the like which include integral balustrades are so described.

- Dimensions and details are stated in descriptions, where necessary, to identify the work.

- Ladders and the like are given in metres.

Work is deemed to include:

- linings, nosing, cover moulds, trims and the like, where supplied with the unit,

Ladders and the like (Cont'd), Work is deemed to include:

- soffit lining, spandrel panels and the like, where supplied with the unit,

- fixings and fastenings including blockings, wedges, bolts, brackets, cleats and the like,

- cutting and fitting around obstructions,

- protective painting, galvanizing and sprayed metal coatings including priming and all other preparatory works carried out at place of fabrication or on site,

- finishes, where part of the item as delivered,

- All painting on site.

ORNAMENTAL HANDRAILS AND RAILINGS

Balustrades and The Like - Generally

- Each kind of work is given separately, stating the kind of material and finish as delivered.

- Each type of balustrades and the like is given separately.

- Each height of balustrades and the like is given separately.  Raking and curved or ornamental work are each so described.

- Balustrades and the like are given in metres.

Work is deemed to include:

- cover moulds, trims, and the like, where supplied with the unit,

- glazing and the like, where supplied with the unit,

Expansion joints and trims (whether expressly required or installed at the discretion of the Contractor),

- ends, ramps, wreaths, bends and the like in balustrades and the like,

- fixings and fastenings including blockings, wedges, bolts, brackets, cleats and the like,

- cutting and fitting around obstructions, integral services, into recesses and the like including additional materials,

- protective painting, galvanizing and sprayed metal coatings including priming and all other preparatory works carried out at place of fabrication or on site,

- finishes, where part of the item as delivered,

- Work of any girth, width or height.

SECTION 4 - FLOOR, WALL & CEILING FINISHINGS

General

A.	Floor, wall and ceiling finishes have been measured nett in square metre or in metres.

B.	Rendering and wall tiling have been measured from top of skirting, (if any) to soffit of slab.  Where there are suspended ceilings, measurements were taken to the soffit of the suspended ceiling plus 100 mm unless otherwise indicated on drawing. All openings and other unfinished areas over 0.5 m2 have been deducted.

Rates shall include for:

C	Waterproofing to kitchen bathrooms and the like have been measured as flat area in m2.

Rates for waterproofing to wet areas is deemed to include for carrying the waterproofing up walls to 100 mm above FFL and upto 100 mm above the edge of bathtubs.

D.	Supplying all materials, protection, storage, plant, equipment and tools, scaffolding, accessories, fixing, mixing and curing and all incidental work necessary for the proper execution of the finishings to the Engineer's satisfaction.

E.	Preparing and submitting samples for approval.

F.	Working narrow widths and short lengths to jambs or reveals, sills, soffits of lintels, sides and soffits of beams, kerbs, upstands and making good.

G.	Attending and making good all work after other trades to the Engineer's satisfaction.

In-Situ Finishings

Rates for In-Situ Finishings shall include for:

H.	Forming horizontal or vertical guide screeds and for supplying hardwood guide blocks.

J.	Preparing surface and providing expanded metal lath at junctions of blockwork and concrete.

K.	Work to curved surfaces.

L.	Work to falls and crossfalls.

M.	Rounded edges, chamfered edges, quirks, arises and the like;

N.	Features, grooves, beaded edges, mounted edges, ends, angles, intersections and the like.

Tile Finishes

Rates for tile slab and sheet finishings shall include for:

A.	Straight and curved cutting, waste, grouting, pointing and the like to execute the works to the satisfaction of the Engineer.

B.	Cutting to shape around fittings, chamfering, leveling and the like and shall include for purpose-made tiles and slabs (ex. rounded edges, coves, etc.).

C	Work to falls and cross falls.

D.	The preparation and furnishing, to the Engineer, of detailed workshop drawings for approval prior to commencement of work and/or ordering of materials.

E.	Providing special tiles for rounded edges, internal and external angles, edge tiles, etc.

F.	Providing required approved sand fill below tile or slab mortar to bring-up levels to the finished floor levels.

Suspended Ceiling Finishing

G.	Suspended ceilings are measured flat. Rates for suspended ceiling shall be deemed to include for all stepping, bulkheads of all heights, edge trims/mouldings, decorative mouldings, light coves, suspension system, etc.

Rates for suspended ceilings shall include for the following:

H.	Submitting samples of the system to the Engineer for approval prior to order.

J.	Forming circular, rectangular or square openings for electric light fixtures, AC ducts and grilles, access panels and for straight cutting, curved cutting and waste.

K.	Cleaning any soiled or discoloured surfaces of units, including the removal and replacement of units which are damaged or improperly installed.

L.	On completion of the installation, cleaning of all areas where suspended ceiling works were executed, of all waste, cuttings, etc.

M.	Preparation and furnishing, to the Engineer, of detailed workshop drawings for approval prior to commencement of work and/or ordering of materials.

N.	Providing access openings, doors/closure panels to the approval of the Engineer.

P.	Providing equal margins when setting out grid and for all standard edge trim details.

SECTION 5 - PAINTING & DECORATION

A.	Painting and decoration works have been measured net in m2.

B.	Openings exceeding 0.50 m2 have been deducted.

Rates for all paint work shall include for:

C. 	Supplying all necessary materials, machines, tools, brushes, etc. scaffolding, ladders, storage and protection, additives, mixing, hoisting, sampling and testing, and all other incidental requirements for the proper execution of paint work as specified.

D.	Cleaning loose render and repairing all cracks and holes with patching render properly keyed to existing and sand-papering smooth.

E.	Neutralising alkaline surfaces of rendered or exposed concrete areas by brushing on, an acid solution and two percent zinc chloride or approved equal and removing all loose particles after drying as directed by the Engineer.

F.	Narrow widths and in short lengths to apertures, jambs, sills, reveals, soffits of lintels, sides and top faces of curbs, panels and strips, etc.  All such areas to be included within their respective main items, unless otherwise stated.

G.	Painting in multi colours as required.

H.	Making good all paint work to the satisfaction of the Engineer.

J.	Rates for paint work on ferrous and non-ferrous metalwork shall include for cleaning with steel wire brushes or scraping as may be necessary to remove all loose scale and rust and all unexposed surfaces of ferrous and non-ferrous metalwork in false ceilings, attics, shafts, etc. shall include for applying two coats of rust inhibiting primer.

K.	Rates for paint work for timber works shall include for rubbing down with glass paper before painting. All exposed surfaces of wood work covered with plywood lining, veneered, etc. shall receive two coats of approved wood preservative as specified.

SECTION 6 - FITTINGS

Corner guards

- Corner guards are enumerated or given in metres as per items in bill of quantities; complete as specified.

Work is deemed to include:

- surface treatments and preservative treatments applied as part of the production process,

- finishes, where part of the item as delivered,

- rebates, grooves, splays, chamfers, mouldings and the like including ends, angles and mitres,

- fixings and fastenings,

- Cutting and fitting around obstructions.

Glazing - Generally

- Each kind of glass is given separately, stating the thickness. Glass with ground, sandblasted, embossed and engraved surfaces are each so described.

- Mirrors are enumerated.

Work is deemed to include:

- All necessary fixings, fittings, furniture, accessories and related works and materials,

- Stainless steel frames,

- Plywood backing

SECTION 7 - EXTERNAL WORKS

Tile Finishes

- Floor finishes have been measured nett in m2.

Rates for tile finishing shall include for:

- Straight and curved cutting, waste, grouting, pointing and the like to execute the works to the satisfaction of the Engineer.

- Cutting to shape around fittings, chamfering, leveling and the like and shall include for purpose-made tiles and slabs (ex. rounded edges, coves, etc.).

- Work to falls and cross falls.

- The preparation and furnishing, to the Engineer, of detailed workshop drawings for approval prior to commencement of work and/or ordering of materials.

- Providing special tiles for rounded edges, internal and external angles, edge tiles, etc.

- Providing required approved sand fill below tile or slab mortar to bring-up levels to the finished floor levels.

- Cleaning of all areas at completion.

CURB (KERBS)

- Each kind of curbs is given separately, stating the kind of material.

- Measurements shall be of the front face of concrete curb or of the flow line                         of gutter as appropriate.

- Excavation, backfilling, bedding, concrete backing, construction in and around obstacles shall not be measured for direct payment, but shall be considered as subsidiary works, the costs of which will be deemed to be included in the contract prices for the pay items.

SECTION 8 - Engineers Office

Immediately upon possession of the site the contractor shall rent an office. Flowing area 50 m2 and, shall provide and maintain this office with warm and cold air-conditioning for the use of Engineer. The office shall be cleaned daily; full time office boy required the Contractor must pay all charges in connection therewith including the provision of all necessary power for the air-conditioners, lights and power points. He shall also provide and pay for, entirely at his own expense, a drinking water supply including tea and coffee

If The contractor fails to provide the office as prescribed within 30 calendar days after issuance of Notice to proceed, the engineer reserves the right to find suitable replacement of temporary site office. All at the expense of the Contractor.